## Slide 1: Autonomous Smart Cart with ROS 2
Team Members (MISIS):
Ashwin Murali Thanalapati (M01037932)
Mohammed Shalaby (M01035318)
Jayashanka Anushan (M01037028)
Vignesh Lakshmanasamy (M01026685)
PDE4435 - Robotic System Integration

## Slide 2: Problem Statement, Background, Motivation, Goals
This project aims to solve unsafe and effort-heavy shopping cart use in crowded retail aisles that will bring safer, easier, and more efficient shopping.
Background: conventional carts require continuous manual force and have no intelligent safety layer.
Motivation: reduce physical strain (elderly/parents) and reduce minor collisions in dense pedestrian flow.
Goals: robust follow-me at 1.0 m, obstacle-safe motion, and integrated ROS 2 simulation for validation.

## Slide 3: Solution Overview (Architecture)
Platform:
ROS 2 Jazzy + Gazebo Harmonic
Architecture:
- Multi-node system using ROS2 topics
Key Modules:
- UWB Simulation → provides position data
- Follow Node → estimates position & smooths data
- Obstacle Node → ensures safety and speed control
- Navigation Logic → manages robot behavior (Idle, Follow, Stop)
Output:
- Final motion command published to /cmd_vel

## Slide 4: Team members contribution
Vignesh – Robot Design & Simulation
Designed CAD model (SolidWorks)
Converted model to URDF
Developed Gazebo simulation environment
Integrated LiDAR sensor
Jay – Control & Navigation
Implemented motion control (/cmd_vel)
Developed follow behaviour logic
Designed navigation state machine (Idle, Follow, Stop)
Ashwin – Sensors & Communication
Developed UWB simulation
Implemented position estimation (trilateration + filtering)
Managed ROS2–Gazebo communication (bridge)
Shalaby – Documentation & Presentation
Structured project report
Managed requirement traceability
Prepared test documentation
Developed presentation materials

## Slide 5: Key Advantages of Our Solution
Layered Safety
Combines long-range tracking (UWB) with short-range obstacle detection (LiDAR)
Safer than single-sensor systems
Fast Response
End-to-end control latency ≈ 5 ms (simulation)
Enables real-time robot reaction
Stable Tracking
Kalman filter improves UWB accuracy
Position error reduced by ~35–40%
Modular Design
Built using ROS2 nodes
Easy to extend (SLAM, ML, real robot)

## Slide 6: System Demonstration
Demo Highlights
Robot successfully spawned in Gazebo environment
Real-time movement using teleoperation (/cmd_vel)
LiDAR scan visualization in RViz (/scan)
Autonomous obstacle avoidance behaviour
What to Observe
Smooth robot motion and control response
Real-time sensor data updates
Robot reacting to obstacles and changing direction

## Slide 7: Testing Results & Evaluation
Successes
Accurate Following
  Distance: 1.04 ± 0.08 m
  Target: 1.0 ± 0.15 m
Reliable Localization
  UWB error < 0.30 m
  After Kalman filter: ~0.07–0.13 m
Safe Obstacle Handling
  Emergency stop at 0.27 ± 0.03 m
  No collisions observed
Limitations
Slight overshoot during sharp turns
Reduced accuracy at longer distances

## Slide 8: Conclusion & Future Work
Conclusion
Core objectives successfully achieved in simulation
Reliable follow-me behaviour with stable tracking
Layered safety system ensured collision-free operation
Low-latency control enabled responsive robot movement
Comparison with Goals
Tracking accuracy within target range ✅
System latency met real-time requirements ✅
Obstacle detection and safety performed reliably ✅
Future Work
Real-world hardware implementation
Improve localisation under multipath conditions
Integrate camera + ML for enhanced interaction
Enhance human–robot interaction (HRI) feedback
Reflection
Modular ROS2 design simplified debugging and testing
Sensor integration improved system robustness
Iterative simulation helped refine system performance

## Slide 9: Thank You
Ashwin Murali Thanalapati (M01037932)
Mohammed Shalaby (M01035318)
Jayashanka Anushan (M01037028)
Vignesh Lakshmanasamy (M01026685)
Any Questions?